## Slide 1
Photo: Maido Obs., Reunion Island (source: G. Payen, OSU-R)
Lidar
G. Ancellet, T. Berkoff, V. Duflot, S. Kuang, A. Langford, T. Leblanc, T. McGee, M. Newchurch, C. Senff, K. Strawbridge, and J. Sullivan
The NDACC and TOLNet Lidar PIs:

## Slide 2
NDACC and TOLNet Tropospheric Ozone Differential Absorption Lidars
NDACC only:
OHP, France: NH mid-lat 1990-present 1.8 - 13 km a.g.l. *
Reunion Island: SH tropics 1998-present 4.0 - 17 km a.g.l. * (Southern Indian Ocean)
TOLNet Only:
TOPAZ NOAA-Boulder: Mobile 2012-present 0.03 - 10 km a.g.l.
LMOL, NASA-LaRC: Mobile 2014-present (0.1) - 12 km a.g.l.
AMOLITE, ECCC Toronto: Mobile 2014-present 0.2 - 15 km a.g.l.
NDACC and TOLNet:
JPL-TMF, California: NH mid-lat 1999-present (0.7) - 22 km a.g.l. *
UAH, Huntsville, Alabama: NH mid-lat 2004-present (0.5) - 15 km a.g.l.
TROPOZ, NASA-GSFC: Mobile 2013-present (0.5) - 15 km a.g.l.
* OHP, Reunion, TMF: Strato. O3 DIAL available for altitudes above 12 km a.g.l.

## Slide 3
Is uncertainty reported consistently for the NDACC and TOLNet lidars?
Total uncertainty: quadratic sum of all components (random and systematic)
Random uncertainty: Signal detection noise
Systematic uncertainty: quadratic sum of the following systematic components: Signal saturation Background noise extraction Ozone absorption cross-section (use of so-called “BDM”) and the following minor components: Molecular extinction cross-section Ancillary air density/temperature/pressure profile NO2 absorption cross-sections Ancillary NO2 profile SO2 absorption cross-sections Ancillary SO2 profile
It is reported consistently, following Leblanc et al., AMT, 2016 guidelines, when the following variables in the NDACC and TOLNet files in HDF (GEOMS) format contain non-missing values:
Uncertainty is not reported consistently in the NDACC files in ASCII (Ames) format
In the HDF (GEOMS) files, when the uncertainty is not estimated following the guidelines of Leblanc et al., AMT, 2016, a fourth uncertainty variable named “originator” is used

## Slide 4
On Systematic Uncertainties…
The term “systematic uncertainty”, in the NDACC and TOLNet lidar case, refers to components that are highly correlated in the vertical dimension as well as in the time dimension.
Their behavior (magnitude, altitude dependence, etc.) might change in time, for example if there is a change in data processor, or a change in the choice of ancillary data source
A typical example is: Using the ozone absorption cross-sections of Paur and Bass during the first 10 years of measurements, and then the BDM dataset for the next 10 years
There is no mechanism in the NDACC and TOLNet reporting system that allows a clear identification of correlation lengths for systematic components

## Slide 5
Internal Consistency: Standardized uncertainty budget (Leblanc et al., AMT, 2016)
Total uncertainty: in black, dash curve
Random uncertainty in red: Depends on instrument hardware
Cross-sec. uncertainty in green: Standardized within NDACC and TOLNet
Mol. ext. uncertainty in blue: Depends on the source of ancillary data

## Slide 6
Data Flagging
There is no data flagging in the NDACC and TOLNet reporting system
See “Proposed Harmonization Activities for 2021” slide
Many years ago, it has been agreed within both the NDACC and TOLNet lidar communities that data quality is essentially determined by the reported uncertainty
Nevertheless, for the sake of a proactive TOAR-II involvement, it is planned to explore the options of designing a flag that can address the TOAR-II needs
One exception to the rule:
The HDF files produced by NDACC (and TOLNet) lidar PIs have a global attribute that can be set to “RD” to indicate that the profiles have been produced for Rapid Delivery (RD)
“RD data” are archived in a separate server at NDACC

## Slide 7
Meta Data / Ancillary Data / A priori Data
Temperature-dependent ozone absorption cross-sections
As part of the NDACC and TOLNet lidar networks homogenization, the consensus is to use the results of University of Reims, a.k.a. BDM (Brion-Daumont-Malicet, 1993-1998)
For proper lidar data processing, the following “ancillary data” are needed:
Air density and temperature profile at the time of measurement
There is no consensus within the networks on which data source to use
NO2 and SO2 profiles and absorption cross-sections
Required only for PBL measurements, if lidar operates at certain wavelengths in the Hartley band
There is no consensus within the networks on which data source to use

## Slide 8
Traceability
Are the NDACC and TOLNet O3 lidars traceable to a common reference?
At hardware level: No
Lasers and optical filters often come from the same manufacturers, but the instrument design is typically custom-made, rarely repeated.
Are the instruments internally consistent?
At data processing level: Yes partially
Three elements of data processing are standardized for all NDACC and TOLNet lidars: the ozone absorption cross-sections (BDM), vertical resolution, and the methodology to compute uncertainty budgets (Leblanc et al., 2016)
Several NDACC and TOLNet lidar data have been analyzed systematically, or on a case-by-case basis, by the same data processor (GLASS from JPL). This effort can be extended for TOAR-II if individual lidar PIs interested.
At programmatic level: Yes, through campaigns
The TOLNet SCOOP (2016) inter-comparison campaign is the best example NDACC campaigns typically involve multiple techniques, but the comparison of multiple tropospheric O3 DIAL did not happen yet

## Slide 9
Example of internal and external consistency: the TOLNet inter-comparison campaign SCOOP
Average difference of 18 ozonesonde coincident profiles
Lidar measurements taken during the first 30-min of ECC flights
All lidars agree within +/-3 ppbv (or 4%)
When: August 2016 Where: JPL-TMF

## Slide 10
Foreseen Harmonization Activities in 2021
1) Creation of a “TOAR-II” Lidar meta-database
Purpose: To list, for each lidar, the status of data, metadata and other metrics relevant to TOAR-II harmonization and analysis efforts.
2) Creation of a TOAR-II-dedicated flag, design is yet TBD
Option 1: Implement a generic flag for the entire profile, for example: flag = 0 Quality not assured flag = 1 Excellent/good/nominal flag = 2 Fair/sub-nominal
Option 2: Implement an altitude-dependent flag to help identify specific issues in the profile, for example: flag = 1 No identified issue flag = 2 Data point impacted by cloud flag = 3 Data point possibly impacted by mis-alignment flag = 4 Data point possibly impacted by background noise interference etc…
3) New incentives using the standardized data processor GLASS
Purpose: Assess/ensure the level of standardization of specific datasets

## Slide 11
What lidar can do, that other techniques can’t...
THANK YOU
Tunable temporal sampling and resolution
Tracking of geophysical features at given location
Objective assessment of geophysical temporal variability